## Slide 1: Lines & Symbols
Aerospace Manufacturing Core Study Guide
“AMCSG-303”
Blueprints & Documents

## Slide 2: Line Styles

## Slide 3: Common Line Types
Object Line:
Hidden Line:
Center Line:
Precedence
Dimension Line:
9 ”
3/4
Extension Lines:
Leader Lines:
Break Lines:
Phantom Lines:
Stitch Lines:
9 ”
3/4
Matt Pierce, 2026
Notes: ChatGPT: make a sample revision block from blueprint for aerospace manufacturing

## Slide 4: USNavy14040A - Standard Line Types (1 of 2)
(PD) U.S. Gov – NAVEDTRA14040A, 2015
Notes: ChatGPT query identified USGovernment public domain document: https://media.defense.gov/2017/Nov/03/2002658619/-1/-1/1/171103-N-ZY182-15347.pdf Figure 2-21 on page 33

## Slide 5: USNavy14040A - Standard Line Types (2 of 2)
(PD) U.S. Gov – NAVEDTRA14040A, 2015
Notes: ChatGPT query identified USGovernment public domain document: https://media.defense.gov/2017/Nov/03/2002658619/-1/-1/1/171103-N-ZY182-15347.pdf Figure 2-21 on page 33

## Slide 6: Section Lines
“In blueprints, Section Lines indicate where an imaginary cutting plane has sliced thru a solid material.” - USNavy 14040A
Hashing = Cut Solid
Aligned Section
(PD) U.S. Gov – NAVEDTRA14040A, 2015
(PD) U.S. Gov – NAVEDTRA14040A, 2015
Notes: ChatGPT query identified USGovernment public domain document: https://media.defense.gov/2017/Nov/03/2002658619/-1/-1/1/171103-N-ZY182-15347.pdf – page 39, Figure 2-35

## Slide 7: Blueprint Symbols

## Slide 8: Blueprint Symbols
“Blueprint symbols are standardized universal marks
used as shorthand code
to save space, reduce errors, and
provide clear, concise, and consistent information
across technical drawings.”
- Dr. Google

## Slide 9: Blueprint Symbol Categories
GD&T Symbols
GD&T = Geometric Dimensioning & Tolerancing
Fastener Symbols
Aircraft Symbols
ChatGPT / Matt Pierce, 2026
ChatGPT / Matt Pierce, 2026
ChatGPT / Matt Pierce, 2026
Notes: ChatGPT: “make a diagram comparing three different aerospace manufacturing blueprint symbol categories:
1. geometric symbols: datum, GD&T symbol, dimensional requirement, datum callouts, part features, related features, surface profile
2. fastener symbols: permanent fasteners, removable fasteners, visible fastener location, phantom fastener location, hidden fastener location, fastener identification using NAS 523 standard and four quadrants, dimensional threaded fasteners, and tooling hole symbol
3. aircraft symbols: centerline symbol, flag note indicator, directional indicator, K or coordinating hole indicator, engineered tooling coordinated surface, station indicators (STA,WL, BL) and numbers identifying distinct from 0, and limited release indicator”

## Slide 10: Datum Definition
Matt Pierce, 2026
“A datum is…
a surface, line, or point
from which a geometric position
is to be determined
or from which a distance is to be measured.”
- US Navy “NAVEDTRA 1404A”
Start measuring or dimensioning from the datum.
A
C
B
Plane / Surface Datum
Point Datum
Axes / Line Datum

## Slide 11: Datum Example #1 - From “USNavy14040A”
A .001
Symbol
Perpendicular
Datum
Ref Plane “A”
Tolerance
Within .001
Example #1:
A B .002 TIR
Concentric
Symbol
Example #2:
Datum
Two Ref Planes
Geometric Characteristic Symbols
(PD) U.S. Gov – NAVEDTRA14040A, 2015
Notes: ChatGPT query identified USGovernment public domain document: https://media.defense.gov/2017/Nov/03/2002658619/-1/-1/1/171103-N-ZY182-15347.pdf (pg 75)

## Slide 12: Datum Example #2 - From “ChatGPT”
ChatGPT / Matt Pierce, 2026
Generated w/ChatGPT (mpierce, 2026)
ChatGPT / Matt Pierce, 2026
Notes: ChatGPT: make a diagram showing what a datum, datum feature, datum feature letters, and datum line are.

## Slide 13: Fastener Symbols
Fastener “Header Style”
Fastener “Type”
Fastener “Location”
ChatGPT / Matt Pierce, 2026
Notes: ChatGPT: make an infographic showing aerospace fastener symbols: permanent vs. removable fastener, visible vs. phantom vs. hidden fastener location, and anything else appropriate for the chart + make them all 2 dimensional, top-down view drawing symbols (same as how "visible", "phantom", and "hidden" fastener locations are done.)

## Slide 14: Fastener NAS 523 Identification Quadrants
ChatGPT / Matt Pierce, 2026
Notes: ChatGPT: make an infographic about "National Aerospace Code 523", specifically it's method of symbolically identifying fasteners thru four quadrants "NW, NE, SW, and SE".
1. NW quadrant shows engineering codes for the fastener (eg: fluid tight fastener, etc.)
2. NE quadrant shows two identification codes (X = diameter of fastener in 1/32s of inch, and N or F as the location of the manufactured head)
3. SW quadrant shows three identification codes (D = Dimple, X = number of sheets to be dimpled, and C = Countersink)
4. SE quadrant shows two identification codes (X = fastener length in 1/16s of an inch, and W = spot weld option)
ChatGPT: make an infographic about NAS 523 symbolic instructions for identifying fasteners. Specifically identify the NW, NE, SW, and SE quadrants. Make it a training poster format. + remove the center circle "NAS 523 Symbol". Make the four white dividing lines intersect in the middle. + Remove the arrowheads from the horizontal gray line in middle of chart. Remove title "Symbolic Instructions for Identifying Fasteners“ + Remove label "SW QUADRANT". Remove label "SE QUADRANT. Remove label "NE QUADRANT"

## Slide 15: Q&A

## Slide 16: Practice Q&A’s (Q1-Q8)
Q1: Name of solid lines that depicts the shape of the part or assembly?
A: Object Lines
Q2: Name of dashed lines that depict hidden surfaces, edges, or hole walls?
A: Hidden Lines
Q3: Name of dash-dot-dash lines that indicate the middle, or symmetric on both sides?
A: Center Lines
Q4: Name of lines that have numeric lengths shown (in inches typically)?
A: Dimension Lines
Q5: Thin lines that drop away 90° from the Dimension Line arrow points to the points they are measuring?
A: Extension Lines
Q6: Cut lines showing on one view what a different view is seeing with a section removed?
A: Section Lines
Q7: Name of standardized universal marks used to save space, reduce errors, and provide consistent info on technical drawings?
A: Blueprint Symbols
Q8: Name of blueprint symbols encompassing datums, part features, surface profiles, etc.?
A: GD&T Symbols: Geometric Dimensioning & Tolerancing

## Slide 17: Practice Q&A’s (Q9-Q16)
Q9: Name of blueprint symbols encompassing fastener details?
A: Fastener Symbols
Q10: Name of blueprint symbols encompassing station indicators, tool surface, flag notes, etc.?
A: Aircraft Symbols
Q11: Name of a surface, a line, or a point that is a starting reference position?
A: Datum
Q12: What quadrant of the NAS 523 shows the engineering fastener code (eg: fluid tight fastener)?
A: NW
Q13: What quadrant of the NAS 523 shows the fastener diameter and location (near/far)?
A: NE
Q14: What size does the NE quadrant fastener diameter "7" represent?
A: 7/32". Number 7 is count of 1/32"s. Diameter = shorter = smaller 1/32.
Q15: What quadrant of the NAS 523 shows dimple, countersink, and # of sheets?
A: SW
Q16: What quadrant of the NAS 523 shows length and spot weld?
A: SE

## Slide 18: Practice Q&A’s (Q17)
Q17: What size does the SE quadrant fastener length "8" represent?
A: 8/16". Number 8 is count of 1/16". Length = longer = bigger 1/16.

## Slide 19: Thank You
Matt Pierce - mpierce710006@gmail.com - linkedin.com/in/mpiercead576/
https://github.com/DataResearchLabs/study_guide_intro_aerospace_mfg